## Slide 1
Task 2.2-2.3: Modified Nusselt number
Based on the preliminary results of Nitish (VITO) for eccentricity
  Case F of Task 2.1/2.2
  Fix Nusselt number in the annulus side
    Numax = 262 (fully concentric pipes)
    Numin = 70 (eccentric pipes)
  Time: tmin – 10 years
  Report:
    Temporal evolution (for all time steps) of outlet pressure, temperature, enthalpy difference, power (P, T, ΔH, Q vs. t)
Injection |  |  | Geometry |  | Tubing |  |  | Casing |  | Rocks |  |  | 
Flow rate Q [kg/s] | Temperature T [°C] | Pressure P [bar] | Depth D [km] | Length L [km] | Diameter d [mm] |  | Conductivity ki [W/m/K] | Diameter d [mm] |  | Gradient gT [°C/km] | Conductivity kr [W/m/K] | Capacity Cpr [J/kg/K] | Density ρr [kg/m3]
 |  |  |  |  | OD | ID |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  | OD | ID |  |  |  | 
8.8 | 45 | 40 | 3 | 3.5 | 0.05 | 0.08 | 0.1 | 0.1778 | 0.1617 | 32.5 | 2.423 | 902.67 | 2600
Case | Nu
1 | 262
2 | 230
3 | 190
4 | 150
5 | 110
6 | 70