## Slide 1
Task 2.2-2.3: Well models (IFE, IFPEN, UNIFI, RW)
Injection |  | Geometry |  | Insulation |  | Casing |  |  |  | Rocks |  | 
Flow rate v [l/s] | Injection temperature T [°C] | Depth D [km] | Length L [km] | Material ki [W/m/K] | Thickness e [mm] | Diameter (vertical) dV [mm] |  | Diameter (horizontal) dH [mm] |  | Gradient gT [°C/km] | Conductivity (vertical) kr [W/m/K] | Conductivity (horizontal) kr [W/m/K]
 |  |  |  |  |  | OD | ID | OD | ID |  |  | 
5 | 25 | 2 | 3 | 0.01 | 5 | 248 | 217 | 178 | 159 | 20 | 1.4 | 2
7.5 | 30 | 3 | 5 | 0.1 | 10.5 | 273 | 253 | 194 | 175 | 30 | 2 | 3
10 | 35 | 4 | 7 | 1 | 15 | 298 | 271 | 219 | 201 | 40 | 3 | 5
GTW (IFE)
GWellFM (IFPEN)
BHEModel (UNIFI)
Water properties: PT dependant
Injection pressure: 10 bar
Surface temperature: 15°C
Domain radius: 50 m
Rocks properties: ρr = 2600 kg/m3, Cpr = 900 J/kg/K
Casing and tubing properties: : ρc = 7850 kg/m3, Cpc = 466 J/kg/K, kc = 50 W/m/K
Fluid model activated
Fully cased, not cemented
Basic case (red squares): Simulated with GTW (IFE), GWellFM (IFPEN) & BHEModel (UNIFI)
Time: tmin – 20 years
Report:
  Temporal evolution (for all time steps) of outlet pressure, temperature, enthalpy difference, power (P, T, ΔH, Q vs. t)
  Spatial evolution of fluid’s pressure, temperature with the distance along the casing and tubing (Pf, Tf vs. l) at 1, 7, 15, 30, 60, 90, 180, 365, 730, 1825, 3650, 7300 days
  Temporal (at above time steps) and spatial (profile along the wellbore) rock’s temperature at 1, 5, 10, 20, 30 m from the horizontal well

## Slide 2
Task 2.2-2.3: Well models (IFE, IFPEN, UNIFI, RW)
Injection |  | Geometry |  | Insulation |  | Casing |  |  |  | Rocks |  | 
Flow rate v [l/s] | Injection temperature T [°C] | Depth D [km] | Length L [km] | Material ki [W/m/K] | Thickness e [mm] | Diameter (vertical) dV [mm] |  | Diameter (horizontal) dH [mm] |  | Gradient gT [°C/km] | Conductivity (vertical) kr [W/m/K] | Conductivity (horizontal) kr [W/m/K]
 |  |  |  |  |  | OD | ID | OD | ID |  |  | 
5 |  | 2 | 3 | 0.01 |  |  |  |  |  |  |  | 
7.5 | 30 | 3 | 5 |  | 10.5 | 273 | 253 | 194 | 175 | 30 | 2 | 3
10 |  | 4 | 7 |  |  |  |  |  |  |  |  | 
GTW (IFE)
GWellFM (IFPEN)
BHEModel (UNIFI)
Injection |  | Geometry |  | Insulation |  | Casing |  |  |  | Rocks |  | 
Flow rate v [l/s] | Injection temperature T [°C] | Depth D [km] | Length L [km] | Material ki [W/m/K] | Thickness e [mm] | Diameter (vertical) dV [mm] |  | Diameter (horizontal) dH [mm] |  | Gradient gT [°C/km] | Conductivity (vertical) kr [W/m/K] | Conductivity (horizontal) kr [W/m/K]
 |  |  |  |  |  | OD | ID | OD | ID |  |  | 
5 |  |  |  | 0.01 | 7.5 | 248 | 217 | 178 | 159 |  | 1.4 | 2
 | 30 |  | 5 |  | 10.5 | 273 | 253 | 194 | 175 | 30 | 2 | 3
 |  | 4 |  |  | 12.5 | 298 | 271 | 219 | 201 |  | 3 | 5
Injection |  | Geometry |  | Insulation |  | Casing |  |  |  | Rocks |  | 
Flow rate v [l/s] | Injection temperature T [°C] | Depth D [km] | Length L [km] | Material ki [W/m/K] | Thickness e [mm] | Diameter (vertical) dV [mm] |  | Diameter (horizontal) dH [mm] |  | Gradient gT [°C/km] | Conductivity (vertical) kr [W/m/K] | Conductivity (horizontal) kr [W/m/K]
 |  |  |  |  |  | OD | ID | OD | ID |  |  | 
5 |  |  |  | 0.01 |  |  |  |  |  | 20 |  | 
 | 30 |  | 5 | 0.1 | 10.5 | 273 | 253 | 194 | 175 | 30 | 2 | 3
 |  | 4 |  | 1 |  |  |  |  |  | 40 |  | 

## Slide 3
Task 2.2-2.3: Well models (IFE, IFPEN, UNIFI, RW)
Tornado diagrams